## Slide 1: The Buried Giant: Construction Materials Shape the Environmental Footprint of Buildings
Dr. Rolf Frischknecht
8th International ICARB Conference 2023
Edinburgh, Scotland, 26 September 2023
Ishiguro 2015

## Slide 2
Zero emissions!

## Slide 3: 4 questions
On whose shoulders do we stand?
Construction materials: the buried giant?
Net zero emission buildings: Castles in the air?
What remains to be done?
Notes: Graue Energie zunehmend wichtig -> bei Neubauten oft wichtiger als gesamte Betriebsenergie über Lebensdauer (SES)
Pariser Abkommen: 1.5 Grad-Ziel -> Fokus Treibhausgasemissionen
CH: 26% der THGe durch Gebäude verursacht
SIA-Fachblatt 2040 (SIA-Energieeffizienzpfad): Ausnahme: individuelle Mobilität (3l/100km)

## Slide 4
Exponential growth in the past:
What policy to adopt?
Prof. William S. Jevons (1835-1882)
Economist and Logician
Born in Liverpool, UK
« We have to make the momentous choice between brief greatness and longer continued mediocrity. »
Jevons (1865)

## Slide 5
Prof. Rudolf Clausius (1822-1888)
Born in Poland
Professor at ETH Zürich
«People will then have to rely on the energy which the sun will continue to supply with its rays in the course of the distant future.»
A more sustainable solution:
Use of renewable energies
Jevons (1865)

## Slide 6
First life cycle considerations
Poor efficiency in coal supply chain
Geddes (1884)
Coal available
Coal lost
Used
Prof. Patrick Geddes (1854-1932)
Born in Scotland
Professor at University Edinburgh

## Slide 7: Seventies: Cumulative energy demand of materials and chemicals
Boustead & Hancock 1979
Notes: Bedeutung der Phase Erstellung nimmt zu:
Metaanalyse von scientific papers zu Carbon footprint von Gebäuden (Autoren: Experten aus dem IEA EBC* Annex 72).
Sample: 650+ Gebäude (Wohnen und Büro) in Europa, Asien und Nordamerika, darunter auch rund 1 Dutzend CH-Gebäude.
Rund 240 in der Analyse verwendet
Einteilung in drei Klassen: Durchschnitt, heutiger Standard und erhöhte Anforderungen
=> Anteil Gebäude-Erstellung (rot, Herstellung der Baumaterialien, -elemente und Haustechnik) hat zugenommen und erreicht bei Gebäuden mit hohem Energiestandard im Schnitt schon 50%
*EBC: Energy in Buildings and Communities Programme

## Slide 8
Eighties: LCA of first zero energy buildings
© srf.ch
Hofstetter et al (1991)

## Slide 9
Eighties: Comparative assessment of insulation materials
Ems et al (1989)

## Slide 10: Nineties: Cornerstone of LCA in buildings LCA Database Switzerland
  ETH Zürich, 1994: “Ökoinventare von Energiesystemen” about 500 Data sets on
    energy supply
    building materials and chemicals
    transport services
    waste management services
Frischknecht et al (1994)

## Slide 11: Noughties: Evolution to ecoinvent and UVEK databases
  ecoinvent Centre, 2003-2008, UVEK Data 2012-today: Online LCA database with about 2500-4000 datasets on
    energy supply
    water supply
    building materials, chemicals, packaging, textiles
    electronics
    mechanical engineering
    transport services
    waste management services
    agriculture

## Slide 12
Fossil CO2 emissions and LCA in the construction sector
Source: IPCC (2013)
180 years (1750-1970): 5 GtCO2 per year
40 years (1971-2011): 30 GtCO2 per year

## Slide 13
ASSESSING OPERATIONAL AND EMBODIED EMISSIONS – CURRENT TRENDS
There is a downward trend in operational emissions relating to an improved energy performance and increasing use of renewable energy.
The relative and absolute values of embodied impacts (here embodied GHG emissions) increase.
The consideration of the entire life cycle, the limitation of the upfront/initial emissions, as well as the development of overall goals and guidance values for operational and embodied GHG emissions are necessary.
Röck et al. 2020

## Slide 14: LCA data for the construction sector in CH The KBOB recommendation 2009/1
Contains LCA data on:
Construction materials
Building technology
Energy supply
Transport services
Waste management services

## Slide 15: System boundary LCI of construction materials
No credits

## Slide 16: LCA data for the construction sector in CH The KBOB recommendation 2022
Total environmental impacts 2021
production
end of life
Primary energy total and Primary energy non renewable
production
end of life
Further distinction in
energetic use
use as raw material
Greenhouse gas emissions
production
end of life
Biogenic carbon content
Further features:
Potential benefits and loads beyond system boundary (module D) excluded
UUID number
company specific datasets available
background LCI database available for SimaPro, openLCA* and Brightway* *expected

## Slide 17: Evolution of the carbon footprint (production and end of life) of construction materials
Evolution | Past
Concrete | ↘
Steel | ↘↘↘
Aluminium | ↘↘
Glass | →
Wood | ↘↘↘
100
740
5600
1200
340
values 2022 in g CO2-eq/kg

## Slide 18: Evolution of the carbon footprint of construction materials
Evolution | Past | Future *
Concrete | ↘ | ↘↘↘
Steel | ↘↘↘ | ↘↘↘
Aluminium | ↘↘ | ↘↘
Glass | → | ↘↘↘
Wood | ↘↘↘ | ↘↘
24
270
2500
260
220
future values in g CO2-eq/kg
* requires substantial industry investments

## Slide 19: Case study buildings
Office building ARE-Ittigen with 96 working places
Minergy-P-ECO
Concrete kernel and wood façade, compact
Heating and hot water: 82 MJ/m2a (electric heat pump)
Ventilation & lighting: 70 MJ/m2a
Residential building Rautistrasse with 104 flats
Minergy-ECO
Massive construction
Heating and hot water : 107 MJ/m2a (electric heat pump)
Ventilation & lighting : 45 MJ/m2a
Notes: Heizung: Wärmepumpe bei beiden Gebäuden

## Slide 20: GHG-Emissions Office building
target values
SIA 2040:2017
Embodied
Embodied and operational
embodied
operational
Notes: D0: Excavation
D1: Backfilling
D2: Foundation
E0: Slabs
E1: Roofs
E2: Pillars
E3: External walls basement
E4: External walls above ground
E5: Windows
E6: Interior walls, load bearing
M1: Partitions / interior doors
M3: Floor coverings
M4: Wall finishes
M5: Ceiling finishes
I: Building technology
9.4kg CO2eq/m2a; 4.6kg CO2eq/m2a (Reduktion um 51%)
Richtwert SIA 2040: 9 + 4 kg CO2eq./m2
Abdeckung Materialen durch zukünftige Produktion: 70%

## Slide 21: GHG-Emissions Residential building
target values
SIA 2040:2017
Embodied
Embodied and operational
embodied
operational
Notes: 11.8kg CO2eq/m2a; 5.1kg CO2eq/m2a (Reduktion um 57%)
Richtwert SIA 2040: 9 + 3 kg CO2eq./m2
Inklusiv Karbonatisierung: Reduktion der THGem um 0.25-2.5%
Abdeckung Materialen durch zukünftige Produktion: 96%

## Slide 22: How does “net zero” work?
HORTUS Building Allschwil/Switzerland
© Herzog & de Meuron
HORTUS pays back its construction energy in one generation. On the BaseLink site in Allschwil near Basel, SENN, Herzog & de Meuron and ZPF Ingenieure are jointly developing an office building with approx. 10,000 m2 of usable space for environmentally conscious (tech) companies. The building sets a new standard for sustainability: it pays back the grey building energy and is already energy-positive after around 30 years. In addition, it is constructed from an unusual mix of natural materials.
Translated with www.DeepL.com/Translator (free version)

## Slide 23: (Net)Zero GHG-emission buildings System boundary
Production, construction, use
and end of life
Operation, energy, all
Operation, energy, regulated
Lützkendorf & Frischknecht (2020)

## Slide 24
Taxonomy of Carbon offsets
(adapted from Oxford Principles 2020)
adapted from Oxford Principles (2020)
How is the offset generated | Is carbon stored | How is carbon stored | Example
Potentially avoided emissions | No | - | Forward-looking, counterfactual baseline: Renewable energy potentially replacing fossil fuels
Emissions reduction | No | - | Clear retrospective emissions data: N2O abatement; Methane abatement
Emissions reduction | Yes | short | Changes to agricultural practices that retain already stored carbon
Emissions reduction | Yes | long | Carbon Capture and Storage (CCS) on industrial facilities, fossil fueled power plants
Carbon removal | Yes | short | Afforestation, reforestation Soil carbon enhancement
Carbon removal | Yes | long | Direct air carbon capture and storage (DACCS) Biogenic energy carbon capture and storage (BECCS) Mineralisation, enhanced weathering

## Slide 25: OPTIONS TO DEFINE AND ACHIEVE (NET) ZERO GHG-EMISSION BUILDINGS
Net Zero emission approaches |  |  |  | Zero emission a.
Net balance | Net balance | Economic compensation | Technical Removal | Absolute Zero
potentially avoided emissions | allocation |  |  | 
Accounting for the potential benefits caused by exported energy produced on-site | Attributes the pro rata share of GHG emissions caused by on-site energy production to the exported energy | Purchase of CO2 certificates based on potentially avoided or reduced GHG emissions | Investment in negative emission technologies to offset life-cycle-based GHG emissions caused by the building | Use of construction materials/operational energy with zero GHG emissions (including supply chain emissions)
Level of effectiveness and thus ambition
-
+
Lützkendorf & Frischknecht (2020)
Lützkendorf & Frischknecht 2020

## Slide 26: Biogenic CO2 from biogas purification used to recarbonise recycled concrete aggregate
Negative Emission Technology with
10 kg CO2 removed per m3 concrete

## Slide 27
Temporal nature based carbon
removal (NbCS)
Sigriswil/BE
© Johanna Frischknecht, 2017
Lower peak temperature increase in ambitious mitigation scenarios
Delay of temperature increase in weak mitigation scenarios
NbCS not an alternative but a complement to the reduction of fossil emissions to net zero by 2050

## Slide 28
Modelling biogenic carbon in buildings
(wood, straw, hemp, etc,)
Sigriswil/BE
© Johanna Frischknecht, 2017
Negative Emission technology
if
multiple reuse of building elements or
permanent sequestration
for at least 3000 to 8000 years
How to ensure:
Legally binding entry in land register:
„Separation and permanent storage“

## Slide 29: Conclusions and recommendations
Buildings and their supply chains are important emitters of CO2 and greenhouse gases
Embodied emissions more and more important despite significant reduction in construction materials production
Further reduction efforts in materials industry needed, in particular cement, steel, glass, aluminium and wood
Negative emission technologies are indispensible to reach net zero emission buildings (and societies)

## Slide 30: Monte Verità Declaration on a built environment within planetary boundaries
39 %
... until 2025 legally binding target values for carbon footprints of buildings with reduction path to net zero by 2035
signed by 40+ experts/researchers from 20 countries in Europe, the Americas and Asia

## Slide 31: Thank you very much for your attention! Contact: frischknecht@treeze.ch Website: www.treeze.ch
Ishiguro 2015
Notes: Let’s dig out the buried giant!

## Slide 32
Growth in the future:
The global average temperature
Jevons (1865)
https://phys.org/news/2019-09-climate-ipcc.html

## Slide 33: Application of KBOB recommendation 2009/1
KBOB recommendation offers average and company specific data
All relevant building related standards refer to KBOB recommendation
Background database relies on ecoinvent protocol v1&2

## Slide 34: LCA data for the construction sector in CH The KBOB recommendation 2006
Total environmental impacts 2006
Primary energy non renewable
Greenhouse gas emissions

## Slide 35: LCA data for the construction sector in CH The KBOB recommendation 2008
Total environmental impacts 2006
Primary energy
- total
- non renewable
Greenhouse gas emissions

## Slide 36: LCA data for the construction sector in CH The KBOB recommendation 2011
Total environmental impacts 2006
production
end of life
Primary energy total and Primary energy non renewable
production
end of life
Greenhouse gas emissions
production
end of life

## Slide 37: LCA on future materials production
Data and information on GHG-emissions and environmental impacts of future construction material production
Establish LCA data on future
    Production of construction materials
    Supply of energy (electricity & fuels)
    Supply of transport services (lorry, train & ship)
preferably compliant with the Paris Agreement 2015 (and the 1.5oC goal)
Contribution of construction materials industry
Notes: Pariser Abkommen: 1.5 Grad-Ziel -> Fokus Treibhausgasemissionen

## Slide 38: Modelling principles
Data acquisition with materials associations and innovative companies, complemented with literature research
Information used to adapt key LCI parameters
No change in recycled content
Thermal energy (fuels) based on biogas and wood
Future electricity mixes of CH, Europe, further countries
Future modes of transportation (electric and biodiesel lorries)
Carbon capture and storage (CCS) applied on CO2-emissionen
Notes: Pariser Abkommen: 1.5 Grad-Ziel -> Fokus Treibhausgasemissionen

## Slide 39: Average concrete CH, production Greenhouse gas emissions
Notes: THGem: -62%
Anpassung Emissionen gemäss Inputs (Primärstahl in EAF, nicht Schrott): Gesamtumweltbelastung reduziert sich auch (-15%)
CED non-renewable: -11%

## Slide 40: Clinker production, CH Greenhouse gas emissions

## Slide 41: Evolution of the carbon footprint of EU electricity mix and PV electricity (low volt.)
Evolution | Past
EU Mix | ↘
Photovoltaics | ↘↘↘
520
55
values 2022 in g CO2-eq/kWh

## Slide 42: Evolution of the carbon footprint of electricity mix and PV electricity
Evolution | Past | Future
EU Mix | ↘ | ↘↘↘
Photovoltaics | ↘↘↘ | ↘↘↘
120
15
future values in g CO2-eq/kWh

## Slide 43: Negative emission technologies

## Slide 44
The effect of potentially avoided emissions explained with “Forged Alliance Forever”

## Slide 45
Potentially avoided emissions require allies
(Illustrated with Forged Alliance Forever)
Gamer Jacob
Gamer Nick
Notes: well-meaning and generous allies

## Slide 46
PV electricity is partly used by the building and partly exported and fed into the grid
Utility purchases exported electricity
Scenario: potentially reduced (or non increase) production of fossil power plants
Potentially avoided emissions (Module D):
Building with Photovoltaic (PV) System
This is not a Negative Emission Technology

## Slide 47
construction materials are expected to be (partly) recycled at end of life
Scrap/secondary raw materials are used to produce construction materials
Scenario: potentially reduced (or non increase) extraction of primary resources
Potentially avoided emissions (Module D):
Materials recycling at end of life
This is not a Negative Emission Technology

## Slide 48
Functional unit:
X m2 floor area
Y kWh
electricity
exported
Building
Utility
Building
Environmental impacts
+
-
Environmental impacts
+
-
PV System
Functional unit:
Y kWh electricity
All impacts caused by the building project are caused by the building and the PV system
PV electricity is partly exported and fed into the grid
Utility purchases exported electricity
Building with Photovoltaic (PV) System Situation (before allocation)

## Slide 49
Functional unit:
X m2 floor area
Building
Building
Environmental impacts
+
-
PV System
Emissions of share of self consumption attributed to building
impacts related to the exported share attributed to electricity
Credit for potentially avoided emissions are outside the system boundary
LCA of complete building split in two (combinable) parts
Building with exporting excess PV electricity Step A&B (ISO 52’000-1) combined
Offsetting position in utility’s electricity supply mix
vermiedene Umweltbe-lastung (Kredit) im Produktsystem 1’ (PV System, Anteil für Export)
Functional unit utility:
Y kWh electricity
Functional unit exported electricity:
Y kWh electricity
Y kWh electricity
exported
excess electricity
Utility
Environmental impacts
+
-
Environmental impacts
+
-
PV System
Building project
exported
PV electricity
in utility mix