## Slide 1
ICARB 2023
Measuring Net Zero
LIVING PLACES
A low-carbon and high-comfort case study in Copenhagen
Ambra Guglietti

## Slide 2
SUSTAINABILITY STRATEGY 2030
Notes: We call our strategy ‘It’s our nature’.
Its meaning is twofold:
Firstly, It is ‘our’ nature to have sustainability at the heart of our business
And secondly, we want to do our part to alleviate climate change and support the nature that we – and all life on earth – rely upon.
2

## Slide 3
SUSTAINABILITY STRATEGY 2030
Notes: We have formulated our strategy as a house. It has three levels, which I will go through now.
Just like when you build a house, I will start with the foundation and end in the attic.
3

## Slide 4
SUSTAINABILITY STRATEGY 2030
Notes: We have set three targets for 2030:
-Show how to build sustainably
-Reduce our future carbon footprint
-Capture our historical carbon footprint
Let me elaborate.
4

## Slide 5
PIONEER CLIMATE AND NATURE ACTION
Show how to build sustainably
Inspire and advocate for sustainable buildings and communities as a strong lever for the green transition and quality of life.
SUSTAINABILITY STRATEGY 2030
Notes: We started to focus on sustainable buildings almost two decades ago.
Through advocacy, demonstration buildings, research and marketing, we have established a strong position, but there's more to be done. ​
​
With this target we will continue to showcase sustainable buildings and communities to ensure a strong influence on the buildings of tomorrow.
In doing so, we will strengthen the long-term relevancy of our products.
5

## Slide 6
SUSTAINABILITY STRATEGY 2030
Build for Life
How we build and transform buildings today has an enormous impact on people and communities, as well as the ecosystems that sustain us tomorrow.
PIONEER CLIMATE AND NATURE ACTION
Extraction
Production
Construction
Use
Renovation
End of life
Beyond
Notes: For our future carbon reductions, we are aligning our targets with climate science as stipulated by the UN’s Climate Panel.
We will commit to the most ambitious reduction pathway of 1.5 degrees for global warming. This is the path set out in the Paris Agreement.
That means we will become a 100% carbon neutral company and reduce the CO2 from our value chain with 50% by 2030.
6

## Slide 7: VELUX demonstration projects
01 | Torzhkovskaya Street St Petersburg, Russia
02 | Soltag Copenhagen,Denmark
03 | Átika Bilbao, Spain
04 | VELUXlab Milan, Italy
05 | VELUX House, COP15 La Rochelle, France
06 | Home for Life Aarhus, Denmark
07 | Green Lighthouse Copenhagen, Denmark
08 | Sunlighthouse Vienna, Austria
09 | LichtAktiv Haus Hamburg, Germany
10 | Maison Air et Lumière Paris, France
11 | CarbonLight Homes Kettering, UK
12 | Osram Culture Centre Copenhagen, Denmark
13 | Guldberg School Copenhagen, Denmark
14 | Albertslund Solar Prism Albertslund, Denmark
15 | Russian Active House Moscow, Russia
16 | Solhuset Hoersholm, Denmark
17 | ISOBO Aktiv Stavanger, Norway
18 | Future Active House Trondheim, Norway
19 | Smith Residence St. Louis, USA
20 | De Poorters Montfoort, the Netherlands
21 | Healthy Home townhouses Stjoerdal, Norway
22 | Multi Comfort House Dzerzhinsk, Belarus
23 | Great Gulf Thorold Toronto, Canada
24 | Optima House Kiev, Ukraine
25 | Langebjerg School Fredensborg, Denmark
26 | Green Solutions House Roenne, Denmark
27 | Solar Decathlon Rome, Italy
28 | LangFang Office Beijing, China
29 | RenovActive Brussels, Belgium
30 | Centennial Park Toronto, Canada
01
03
04
05
08
09
10
11
15
17
19
18
20
21
23
27
29
02, 06, 07, 12, 13, 14, 16, 25, 26, 32
24
22
30
31 | RenovActive House Slovakia
32 | Living Places Copenhagen Copenhagen, Denmark
31
Notes: Main script:
Experimenting is in the DNA of the VELUX Group and conclusions from our full-scale building experiments show that it's possible to build sustainable and healthy buildings using the standard materials, methods and technologies that are available today – proving that energy efficiency and quality of life can go hand in hand.
Additional information:
www.velux.com/what-we-do/healthy-buildings-focus/demonstration-buildings

## Slide 8
NEW BUILD
RENOVATION
TRANSFORMATION
Compass - a strategic approach for both renovation and new build
The approach can be used for new build, transformation and renovations. It serves as a strategic way of thinking which outlines a clear framework to guide the building and development process.
Most of all, the Compass lays out a series of building principles to ensure quality and integrity throughout the entire design process.
The compass model
Notes: 8

## Slide 9
9
SUSTAINABILITY STRATEGY 2030
PIONEER CLIMATE AND NATURE ACTION
LIVING PLACES
SUSTAINABLE LIVING ENVIRONMENTS FOR PEOPLE AND PLANET

## Slide 10
Living Places

## Slide 11
INSIDE
11
Inside the buildings the sloped roof enables better daylight conditions with light from roof windows reaching deeper into the plan. Using double high spaces with skylights we enable better lighting conditions for the lower floors where daylight is most scarce. Moreover, it enables the stack effect of warm air for natural ventilation through overhead windows.
OUTSIDE
Outside at a community scale the sloped roof enables direct sunlight to reach surrounding urban spaces as well as the facades of neighboring buildings. Breaking the façade with sloped roofs helps to scale down buildings towards their surrounding urban spaces. This enables higher density, while maintaining a human scale and enhancing daylight conditions.
Revitalizing the sloped roof

## Slide 12
Principles for Living Places
12
Notes: We developed five key principles:
HEALTHY
SHARED
SIMPLE
ADAPTIVE
SCALABLE
12

## Slide 13
TYPICAL SINGLE FAMILY HOUSE
Size:
Floors:
Building principle: Foundation:
Floor height: Room height:
Heating application: Heating source: Ventilation:
Solar pannels:
Size:
Floors:
Building principle: Foundation:
Floor height: Room height:
Heating application: Heating source: Ventilation:
Solar pannels:
184
1
Brick Concrete
2.7 m
2.4 m
District heating Floor heating Mechanical
7 m²
144
3
Timberframe construction Screw pile foundation
3 m
2.6 m
Air to water heat pump Radiators
Natural or hybrid 12 m²
How we build today
How we might build in the future
LIVING PLACES CONCEPT
How we benchmarked
13

## Slide 14
Carbon CO2 EQ/m2/y:
  From 12 to 3.8
Indoor climate CLASS
  From III to I
Results:
3x lower LCA
14

## Slide 15
OUR LIVING PLACES SCIENCE TALK I 070923

## Slide 16
Health impact

## Slide 17
17
Environmental impact
The diagram compares the CO2 emissions of the full life cycle of the Benchmark house and the Living Places house.

## Slide 18: Simple LCA comparison tool
41
34
21
33
22
42
26
73
69
53
62
74
47
19
76
143
321
9
57
23
61
76
28
42
42
40
38
22
17
25
30
73
42
98
23
7
53
4
33
28
20
77
56
102
63
29
29
9
20
12
0
11
33
43
13
52
22
L-element (polystyrene+ concrete)
Strip foundation in leca and concrete
Rockwool RedAir
Plaster
Wooden cladding, painted
Modular skylight, 3-layer glass
Cell block brick
54
12
29
18
16
18
Strip foundation in leca & concrete with FutureCem
Screw piles
Lightweight wooden cassette, raised
Wooden cassette with glass wool
Lightweight deck on polystyrene
Wooden cassette with cellulose insulation
Lightweight deck on Rockwool Terrain bats
Heavy concrete deck on polystyrene
Wooden cassette w/ I-beams and wood ber insulation
Wooden frame with glass wool + 2 x plaster
Wooden frame with wood ber + 2 x plaster
Wooden frame with
wood ber + OSB & plaster
CLT, 60 mm
Wooden frame with wood ber + 1 x plaster
Ribbed deck with visible beams
Ribbed deck with visible glulam beams
Ribbed deck with plaster ceiling
CLT deck
Steel frame with
glass wool + 2 x plaster
Asphalt roo ng
Steelplates, sinus
Roof tiles
Untreated wooden slats on asphalt roo ng
Slate
Wooden cladding, untreated
Aerated concrete
Lightweight wooden cassette with cellulose insulation
Wood / aluminum
windows (incl. 3-layer glass)
GGL with aluminum & wood (incl. 3-layer glass)
Thin film
Natural ventilation
CLT with cellulose insulation
Barred construction with ventilated attic
Wood / wood windows (incl. 3-layer glass)
GGU with aluminum, PU (incl. 3-layer glass)
Aluminum windows (incl. 3-layer glass)
Modular skylight, 2-layer glass
Efficient solar cells from First Solar
Mechanical ventilation
Highly efficient solar cells from Sunpower
PVC windows (incl. 3-layer glass)
Heavy concrete deck w/ FutureCem on polystyrene
Heavy concrete deck w/ Future- Cem on Rockwool Terrain bats
Wooden cassette with Hempcrete
CLT with cellulose insulation
Heavy concrete back wall
Cell block brick
Wood cladding, untreated
Wood cladding, heat treated
Wood cladding, painted
Sinus plate, steel
+ zinc magnesium
Facade tiles
Slate
Fiber cement
Wooden cladding, heat treated
During the investigation and development of the project, we as a team have created an LCA calculator that provides an overview of solutions and their environmental impact. The calculator simulates building performance based on material choices.
Ventilation
Foundation | Terrain deck | Exterior wall | Exterior wall | Interior | Floor decks | Roof | Roof | Windows | Solar cells
 |  | construction | cladding | walls |  | construction | cladding |  | 

## Slide 19: Simple LCA comparison tool - Benchmark house
41
34
21
33
22
42
26
73
69
53
62
74
47
19
76
143
321
9
57
23
61
76
28
42
42
40
38
22
17
25
30
73
42
98
23
7
53
4
33
28
20
77
56
102
63
29
29
9
20
12
0
11
33
43
13
52
22
L-element (polystyrene+ concrete)
Strip foundation in leca and concrete
Strip foundation in leca & concrete with FutureCem
Screw piles
Lightweight wooden cassette, raised
Wooden cassette with glass wool
Lightweight deck on polystyrene
Wooden cassette with cellulose insulation
Lightweight deck on Rockwool Terrain bats
Heavy concrete deck on polystyrene
Wooden cassette w/ I-beams and wood ber insulation
Wooden frame with glass wool + 2 x plaster
Wooden frame with wood ber + 2 x plaster
Wooden frame with
wood ber + OSB & plaster
CLT, 60 mm
Wooden frame with wood ber + 1 x plaster
Ribbed deck with visible beams
Ribbed deck with visible glulam beams
Ribbed deck with plaster ceiling
CLT deck
Steel frame with
glass wool + 2 x plaster
Asphalt roo ng
Steelplates, sinus
Roof tiles
Untreated wooden slats on asphalt roo ng
Slate
Wooden cladding, untreated
Aerated concrete
Lightweight wooden cassette with cellulose insulation
Wood / aluminum
windows (incl. 3-layer glass)
GGL with aluminum & wood (incl. 3-layer glass)
Thin film
Natural ventilation
CLT with cellulose insulation
Barred construction with ventilated attic
Wood / wood windows (incl. 3-layer glass)
GGU with aluminum, PU (incl. 3-layer glass)
Aluminum windows (incl. 3-layer glass)
Modular skylight, 2-layer glass
Efficient solar cells from First Solar
Mechanical ventilation
Highly efficient solar cells from Sunpower
PVC windows (incl. 3-layer glass)
Heavy concrete deck w/ FutureCem on polystyrene
Heavy concrete deck w/ Future- Cem on Rockwool Terrain bats
Wooden cassette with Hempcrete
CLT with cellulose insulation
Heavy concrete back wall
Cell block brick
Wood cladding, untreated
Wood cladding, heat treated
Wood cladding, painted
Sinus plate, steel
+ zinc magnesium
Facade tiles
Slate
Fiber cement
Wooden cladding, heat treated
Rockwool RedAir
Plaster
Wooden cladding, painted
Modular skylight, 3-layer glass
Cell block brick
54
12
29
18
16
19
The diagram shows the materials used in a traditional Benchmark house and what the environmental impact of this home is.
BENCHMARK HOUSE STRUCTURAL SYSTEM
LCA: 11,1 kg CO₂eq/m²/y
FOUNDATION
Strip foundation in leca and concrete
TERRAIN DECK
Heavy concrete structure
EXTERIOR WALL CONSTRUCTION
Heavy concrete back wall
Brick
INTERIOR WALLS
Aerated concrete
ROOF
Barred construction with ventilated attic
Roof tiles
WINDOWS
Wood / aluminum windows (incl. 3-layer glass)
SOLAR CELLS
Efficient solar cells from First Solar
VENTILATION
Mechanical ventilation
Ventilation
Foundation | Terrain deck | Exterior wall | Exterior wall | Interior | Floor decks | Roof | Roof | Windows | Solar cells
 |  | construction | cladding | walls |  | construction | cladding |  | 

## Slide 20: Simple LCA comparison tool - Living places Timber frame
41
34
21
33
22
42
26
73
69
53
62
74
47
19
76
143
321
9
57
23
61
76
28
42
42
40
38
22
17
25
30
73
42
98
23
7
53
4
33
28
20
77
56
102
63
29
29
9
20
12
0
11
33
43
13
52
22
L-element (polystyrene+ concrete)
Strip foundation in leca and concrete
Strip foundation in leca & concrete with FutureCem
Screw piles
Lightweight wooden cassette, raised
Wooden cassette with glass wool
Lightweight deck on polystyrene
Wooden cassette with cellulose insulation
Lightweight deck on Rockwool Terrain bats
Heavy concrete deck on polystyrene
Wooden cassette w/ I-beams and wood ber insulation
Wooden frame with glass wool + 2 x plaster
Wooden frame with wood ber + 2 x plaster
Wooden frame with
wood ber + OSB & plaster
CLT, 60 mm
Wooden frame with wood ber + 1 x plaster
Ribbed deck with visible beams
Ribbed deck with visible glulam beams
Ribbed deck with plaster ceiling
CLT deck
Steel frame with
glass wool + 2 x plaster
Asphalt roo ng
Steelplates, sinus
Roof tiles
Untreated wooden slats on asphalt roo ng
Slate
Wooden cladding, untreated
Aerated concrete
Lightweight wooden cassette with cellulose insulation
Wood / aluminum
windows (incl. 3-layer glass)
GGL with aluminum & wood (incl. 3-layer glass)
Thin film
Natural ventilation
CLT with cellulose insulation
Barred construction with ventilated attic
Wood / wood windows (incl. 3-layer glass)
GGU with aluminum, PU (incl. 3-layer glass)
Aluminum windows (incl. 3-layer glass)
Modular skylight, 2-layer glass
Efficient solar cells from First Solar
Mechanical ventilation
Highly efficient solar cells from Sunpower
PVC windows (incl. 3-layer glass)
Heavy concrete deck w/ FutureCem on polystyrene
Heavy concrete deck w/ Future- Cem on Rockwool Terrain bats
Wooden cassette with Hempcrete
CLT with cellulose insulation
Heavy concrete back wall
Cell block brick
Wood cladding, untreated
Wood cladding, heat treated
Wood cladding, painted
Sinus plate, steel
+ zinc magnesium
Facade tiles
Slate
Fiber cement
Wooden cladding, heat treated
Foundation | Terrain deck | Exterior wall | Exterior wall | Interior | Floor decks | Roof | Roof | Windows | Solar cells
 |  | construction | cladding | walls |  | construction | cladding |  | 
Ventilation
TIMBER FRAME STRUCTURAL SYSTEM
LCA: 3,8 kg CO₂eq/m²/y
FOUNDATION
Screw piles
TERRAIN DECK
Lightweight wooden cassette, raised
EXTERIOR WALL CONSTRUCTION
Wooden cassette with cellulose insulation
Wood cladding, untreated
INTERIOR WALLS
Wooden frame with wood fiber + 1 x fiber gypsum or plywood per. side
FLOOR DECKS
Ribbed deck with visible beams
ROOF
Lightweight wooden cassette with cellulose insulation
Steelplates, sinus
WINDOWS
Wood / wood windows (incl. 3-layer glass)
GGL with aluminum & wood (incl. 3-layer glass)
Modular skylight, 3-layer pane
SOLAR CELLS
Highly efficient solar cells from Sunpower
VENTILATION
Natural ventilation
Rockwool RedAir
Plaster
Wooden cladding, painted
Modular skylight, 3-layer glass
Cell block brick
54
12
29
18
16
The diagram shows the choices we have made for the timber frame building system and what the environmental impact of this home would be.
20

## Slide 21: Simple LCA comparison tool - Living places C L T
41
34
21
33
22
42
26
73
69
53
62
74
47
19
76
143
321
9
57
23
61
76
28
42
42
40
38
22
17
25
30
73
42
98
23
7
53
4
33
28
20
77
56
102
63
29
29
9
20
12
0
11
33
43
13
52
22
L-element (polystyrene+ concrete)
Strip foundation in leca and concrete
Strip foundation in leca & concrete with FutureCem
Screw piles
Lightweight wooden cassette, raised
Wooden cassette with glass wool
Lightweight deck on polystyrene
Wooden cassette with cellulose insulation
Lightweight deck on Rockwool Terrain bats
Heavy concrete deck on polystyrene
Wooden cassette w/ I-beams and wood ber insulation
Wooden frame with glass wool + 2 x plaster
Wooden frame with wood ber + 2 x plaster
Wooden frame with
wood ber + OSB & plaster
CLT, 60 mm
Wooden frame with wood ber + 1 x plaster
Ribbed deck with visible beams
Ribbed deck with visible glulam beams
Ribbed deck with plaster ceiling
CLT deck
Steel frame with
glass wool + 2 x plaster
Asphalt roo ng
Steelplates, sinus
Roof tiles
Untreated wooden slats on asphalt roo ng
Slate
Wooden cladding, untreated
Aerated concrete
Lightweight wooden cassette with cellulose insulation
Wood / aluminum
windows (incl. 3-layer glass)
GGL with aluminum & wood (incl. 3-layer glass)
Thin film
Natural ventilation
CLT with cellulose insulation
Barred construction with ventilated attic
Wood / wood windows (incl. 3-layer glass)
GGU with aluminum, PU (incl. 3-layer glass)
Aluminum windows (incl. 3-layer glass)
Modular skylight, 2-layer glass
Efficient solar cells from First Solar
Mechanical ventilation
Highly efficient solar cells from Sunpower
PVC windows (incl. 3-layer glass)
Heavy concrete deck w/ FutureCem on polystyrene
Heavy concrete deck w/ Future- Cem on Rockwool Terrain bats
Wooden cassette with Hempcrete
CLT with cellulose insulation
Heavy concrete back wall
Cell block brick
Wood cladding, untreated
Wood cladding, heat treated
Wood cladding, painted
Sinus plate, steel
+ zinc magnesium
Facade tiles
Slate
Fiber cement
Wooden cladding, heat treated
The diagram shows the choices we have made for the CLT building system and what the environmental impact of this home would be.
Ventilation
CLT
STRUCTURAL SYSTEM
LCA: 3,9 kg CO₂eq/m²/y
FOUNDATION
Screw foundation
TERRAIN DECK
Lightweight wooden cassette
EXTERIOR WALL CONSTRUCTION
CLT with cellulose insulation
Wood cladding, untreated
INTERIOR WALLS
CLT
FLOOR DECKS
CLT deck
ROOF
CLT with cellulose insulation
Zink magnesium & asphalt roofing
WINDOWS
Wood / aluminum windows (incl. 3-layer glass)
GGL with aluminum cladding, wood (incl. 3-layer pane)
Modular skylight, 3-layer pane
SOLAR CELLS
Highly efficient solar cells from Sunpower
VENTILATION
Mechanical ventilation
Rockwool RedAir
Plaster
Wooden cladding, painted
Modular skylight, 3-layer glass
Cell block brick
54
12
29
18
16
21
Foundation | Terrain deck | Exterior wall | Exterior wall | Interior | Floor decks | Roof | Roof | Windows | Solar cells
 |  | construction | cladding | walls |  | construction | cladding |  | 

## Slide 22: Life cycle phases
A1 A2 A3
Raw material supply
Transport
Manufacturing
Product
A4 A5
Transport
Construction/ Installation process
Construction process
Use
Maintenance
Repair
Use
Refurbishment
B1 B2 B3 B4 B5
Replacement
Operational energy use
B6
Operational water use
B7
Deconstruction/ Demolition
Transport
Waste processing
End of life
C1 C2 C3 C4
Disposal
D
Reuse, recycle and recovery potential
Benefits beyond system boundaries
Based on data
Based on assumptions
Mandatory phases
Voluntary phases
Excluded phases
The consideration period is 50 years and includes phases A1-A3, B4, B6 and C3-C4. The calculation completely follows the calculation method that from 2023 must be used to document the climate requirements in the Building Regulations in Denmark.
The result of the calculation is given in the unit "kg CO2eq./m² year". The climate load is divided by the building's heated area of 147 m2 (gross area) and the 50 years of lifetime.
The calculation was carried out in the Danish compliant software LCAbyg and lifetimes of materials follow BUILD's lifetime table (AAU). The calculation is also verified by BUILD.
22

## Slide 23: Optimization on each component
kg CO2eq / m² / year
3
2
1
0
TERRAIN BUILD UP
WINDOW & DOORS
INNER WALL
SOLAR PANELS
LEVEL BUILD-UP
INT.
FITTINGS
-100%
-89%
-62%
-92%
-48%
-25%
-81%
+44%
-72%
+100%
-%
Diagram showing the comparison between each element. This shows where we get the biggest savings.
OPERATIONS
OUTERWALLS
FOUNDATION
ROOF
INSTALATIONS
23

## Slide 24: Preconditions
Typology: Construction: Ventilation: Heating:
LCA method: Tool: Dataquality:
One family house
Timber frame and screw pile foundations
Natural ventilation
Heat pump (air to water) with radiators
Danish Building regulations 2023
LCAbyg; product specific + generic EPDs
3. Party verified by AAU / BUILD
3.8 kg CO2 eq/m2/y
Results:
Side 24
24

## Slide 25
φsense – Phygital and Cognitive Paradigm for activehouse In-Use Rating
Effects on Comfort during Sustainable Operational Management Practices Estimated via IoT Devices in a Multi-purpose and BIM-Based Framework.
Supervisor: Prof. Eng. Marco Imperadori
Co-Supervisor: Arch. Lone Feifer
Monitoring Collaboration
PhD student: Nicole di Santo

## Slide 26: Monitoring of the timber frame and CLT buildings of Living Places
26

## Slide 27: Monitoring outcomes from the Active House IN-use assessment
Overall score 1.3
CLT – Hybrid ventilation case
27

## Slide 28: Monitoring outcomes from the Active House IN-use assessment
Overall score 1.4
Timber frame – Natural ventilation case
28

## Slide 29: Monitoring outcomes from the Active House IN-use assessment
The results of this experiment indicate that:
The actual IAQ performances are at the best level according to the active house protocol 3.0 compared to simulated data. Lower values suggest an empty indoor space.
The thermal environment appears to achieve better building performance in the building with hybrid ventilation, confirming the simulated/predicted performances. Higher scores demonstrate the free contribution to heat gains.
As the buildings are not occupied, any evaluation feedback was performed to compare measured and perceived comfort performances.
29

## Slide 31
31
ambra.guglietti@velux.com