## Slide 1: Merging the metrics for financial and carbon accounting
Jimmy Jia
Oxford Sustainable Finance Group
Oxford Net Zero
jimmy.jia@ouce.ox.ac.uk
8th International ICARB Conference 2023
25 Sept 2023
Notes: NB: You can change the background image for this title page in the ‘slide master’ view (you can’t change it directly on this slide)
To add new slides, right click on your slide list and select a new slide from the layout options.

## Slide 2: How much GHG?
Source: https://ourworldindata.org/greenhouse-gas-emissions
Accounting for Global Emissions
Accounting for National Emissions
Accounting for Corporate Emissions
https://www.researchgate.net/publication/264703343_Enhancing_Corporate_Environmental_Performance_Through_Reporting_and_Roadmaps
Notes: POINT: How the financial community defines comparability is different than how the environmental community defines comparability!
SUPPORT:
TRANSITION:

## Slide 3: How much GHG?
Source: https://ourworldindata.org/greenhouse-gas-emissions
Accounting for Global Emissions
Accounting for National Emissions
Accounting for Corporate Emissions
https://www.researchgate.net/publication/264703343_Enhancing_Corporate_Environmental_Performance_Through_Reporting_and_Roadmaps
Based on IPCC methodologies
Based on Life Cycle Assessment (LCA) methodologies
Notes: POINT: How the financial community defines comparability is different than how the environmental community defines comparability!
SUPPORT:
TRANSITION:

## Slide 4: What is financial decision usefulness?
Source: Glenk 2023
Notes: POINT: How the financial community defines comparability is different than how the environmental community defines comparability!
SUPPORT:
TRANSITION:

## Slide 5: What is decision usefulness?
Source: Glenk 2023
Notes: POINT: How the financial community defines comparability is different than how the environmental community defines comparability!
SUPPORT:
TRANSITION:

## Slide 6: What is comparability?
Financial Comparability
The accounting profession emphasizes comparability as a core principle of the financial reporting system.
Formally: “Similar information about other entities and with similar information about the same entity for another period or another date,” (IASB, 2018)
To tell what is similar and what is different between items being compared.
GHG “Comparability”
GHG accounting emphasises consistency as a means to enable comparisons over time.
Formally: “CONSISTENCY Use consistent methodologies to allow for meaningful comparisons of emissions over time. Transparently document any changes to the data, inventory boundary, methods, or any other relevant factors in the time series” (GHG Protocol)
To tell how a single thing changes over time.
Notes: POINT: How the financial community defines comparability is different than how the environmental community defines comparability!
SUPPORT:
TRANSITION:

## Slide 7: What’s been built on top of GHG accounting
Model: Emissions = Activity Data x Emission Factor
Disclosure standards: TCFD, CDP, GRI, ISSB, ICLEI
GHG accounting standards: GHG Protocol
Net zero policies
UN-HLEG, TPT,
ISO IWA 42
Regulations
SFDR, CSRD
Laws
EU Taxonomy
Commercial applications
Ratings, EFTs, M&A
Alliances
GFANZ, NZAOA
Notes: POINT: The non comparability challenges is buried deeply into the modelling equations for carbon emissions.
SUPPORT:
TRANSITION:

## Slide 8: What’s been built on top of GHG accounting
Model: Emissions = Activity Data x Emission Factor
In (Jia et al 2023) we show how all GHG accounting standards reference the GHG Protocol, either directly or indirectly
Disclosure standards: TCFD, CDP, GRI, ISSB, ICLEI
GHG accounting standards: GHG Protocol
Net zero policies
UN-HLEG, TPT,
ISO IWA 42
Regulations
SFDR, CSRD
Laws
EU Taxonomy
Commercial applications
Ratings, EFTs, M&A
Alliances
GFANZ, NZAOA
In (Glenk 2023) showed that GHG Protocol does not follow the rules for financial decision usefulness
In (Jia & Taylor 2022) we show how non-comparability is introduced in the choice of emission factors
Notes: POINT: The non comparability challenges is buried deeply into the modelling equations for carbon emissions.
SUPPORT:
TRANSITION:

## Slide 9: Prior work: Designing for Comparability
Emissions
Activity Data
Operational data (gallons, miles, kWh)
Tells us if the company is operating efficiently
What investors need to know!
An accounting choice, based on combustion, LCA, EEIO, or other estimates.
Values can differ by 38%, because existing standards gives flexibility to choose!
Emission Factor
We can’t tell the difference between operational differences and accounting choices
LCA = life cycle assessment
EEIO = environmentally extended input/output
Source: Jia & Taylor 2022

## Slide 10: Prior work: Designing for Comparability
Emissions
Activity Data
Operational data (gallons, miles, kWh)
Tells us if the company is operating efficiently
What investors need to know!
An accounting choice, based on combustion, LCA, EEIO, or other estimates.
Values can differ by 38%, because existing standards gives flexibility to choose!
Emission Factor
LCA = life cycle assessment
EEIO = environmentally extended input/output
We can’t tell the difference between operational differences and accounting choices
25 September, 2023
Conditions for comparability:
Account for activity data separate from Emission Factor – (Accounting Condition)
Use only Combustion Emission Factors – (Dimensional Analysis Condition)
Account for energy before accounting for carbon
Source: Jia & Taylor 2022

## Slide 11: A difference in accounting for time
In LCA, time passes between events, regardless of how long it takes.
This is known as single entry bookkeeping
Raw material supply
Manufacturing 1
Transport
Transport
Use stage
Production
Transport
Waste processing
Disposal
Usage / Maintenance
Repair
End of life
Manufacturing 2
Transport
In financial accounting, reports are disclosed in regular time periods, regardless of what happens.
This uses double entry bookkeeping
Year 1
Year 2
Year 3
Year 4
Year 5
Year 6
Year 7
Year 8
…
Source: Jia & Taylor 2022

## Slide 12: The Information Architecture to account for time
In LCA, time passes between events, regardless of how long it takes.
This is known as single entry bookkeeping
Raw material supply
Manufacturing 1
Transport
Transport
Use stage
Production
Transport
Waste processing
Disposal
Usage / Maintenance
Repair
End of life
Manufacturing 2
Transport
In financial accounting, reports are disclosed in regular time periods, regardless of what happens.
This uses double entry bookkeeping
Year 1
Year 2
Year 3
Year 4
Year 5
Year 6
Year 7
Year 8
…
Conditions for comparability:
Account for activity data separate from Emission Factor – (Accounting Condition)
Use only Combustion Emission Factors – (Dimensional Analysis Condition)
Use DEBK to synchronize time and accrual accounting to accumulate energy/carbon footprint (Category Theory)
Account for energy before accounting for carbon
Source: Jia & Taylor 2022

## Slide 13: From Single to Double entry bookkeeping in accounting: Cash is in balance
 | Single entry bookkeeping (SEBK) | Double entry bookkeeping (DEBK)
Currencies (Goldthwaithe 1985) | Reports can be in different currencies (Venetian Lira, French Franc, etc.) | All reports needs to be converted to a single currency (Dollars, Euros, etc.)
Accounting Books (Sangster 2016) | Debit / Credit | Debit / Credit Cash / Merchandise / Expenses
Treatment of Time (Quattrone 2005) | Time is recorded as ‘between activities’ | Time is synchronized into periods.
Profit and Wealth (Goldthwaithe 1985) | Merchant had to take inventory each time they wanted to calculate wealth. | Enables the periodic reporting of profit and wealth
Regulation (Sangster 2016) | Complied with Usury laws of the Catholic Church because it was easier to hide profit and wealth. | Complies with financial disclosure and audit rules and regulations.
Source: Jia & Taylor 2023

## Slide 14: An Energy Balance Sheet system: Energy is in Balance
25 September, 2023
 | LCA (and GHGI) is Single-Entry | EBS is Double-Entry
Currencies | LCA can be done for any unit (kWh, Joules, BTU, etc.) | Propose to standardize to Million Joules (MJ)
Accounting Books | Inflow / Outflow | Inflow / Outflow Intrinsic / Embodied / Operational
Treatment of Time | LCA is a summation of activities over time, based on an action taken | EBS synchronizes activities into time periods.
Valuations | Inventory needs to be repeated at every step of the value chain | Enables the periodic reporting of inventory at any step of the value chain.
Regulation | Disclosure regulations ask for GHG Inventories | Enables alignment with IFRS Conceptual Framework (matching, conservatism, etc.)
Auditability (Power 2021) | Not auditable at the moment (can perform limited assurance) | Feeds into the ‘meta-logic’ of the audit trail.
Additivity | LCAs do not add up into a national inventory, unlike corporate activities to GDP | The summation of corporate activities will equal national inventories.
Comparable (Jia & Taylor 2022) | Unable to compare | Ability to tell apart similarities and differences
We also gain:
Source: Jia & Taylor 2023

## Slide 15: The 3 financial reports: (1) Balance Sheet
Balance Sheet
(Present)
Assets
Liabilities
Equity
A balance sheet is a snapshot in time that represents a balance:
Assets = Liability + Equity
NOTE: Cash is a type of Asset
Cash

## Slide 16: The 3 financial reports: Time
Balance Sheet
(Present)
Balance Sheet
(Past)
Cash
Assets
Liabilities
Equity
Equity
Cash
time
Two balance sheets represent the passage of time

## Slide 17: The 3 financial reports: (2) Cash Flow Statement
Balance Sheet
(Present)
Balance Sheet
(Past)
Cash
Assets
Liabilities
Cash
(2) Statement of Cash Flow
(Ending balance sheet) – (Beginning balance sheet)
time
The cash flow statement depicts the change in cash between two balance sheets.
Equity
Equity

## Slide 18: The 3 financial reports: (3) Profit & Loss Statement
Balance Sheet
(Present)
Balance Sheet
(Past)
Cash
Assets
Liabilities
(3) Statement of Profit & Loss
Cash
(2) Statement of Cash Flow
(Ending balance sheet) – (Beginning balance sheet)
Depicts inflows and outflows due to sales
time
Equity
The Profit & Loss depicts a sale transaction between two entities. If there are no sales, there is no P&L.
Equity

## Slide 19: From Single to Double entry bookkeeping in accounting
Energy Balance Sheet
(Present)
time
Energy Balance Sheet
(Past)
Cash
Energy Assets
Liabilities
Lock-in
(3) Statement of Profit & Loss
Cash
(2) Statement of Cash Flow
Energy Flow
Gains and Uses
Energy
Energy
Equity
Energy
Dependencies
Energy
Lock-In

## Slide 20: From Single to Double entry bookkeeping in accounting
Energy
Energy Assets
Energy
(2) Statement of Energy Flow
We will construct the Asset Stack of the Energy Balance Sheet
Energy Flow Statement is the difference between two balance sheets
Assume before commercial start – all transactions are capitalized (No Gains & Use Statement)
We will show how energy shifts up and down the asset stack.
(Ending balance sheet) – (Beginning balance sheet)

## Slide 21: Constructing the Energy Balance Sheet

## Slide 22: Definitions: Intrinsic Energy
Coal stores Chemical Energy
Intrinsic energy: amount of energy stored that is capable of being used later. (Electric energy and equivalents)
Accounting equivalent: Cash and cash equivalents stored inside a bank account, money market account, etc.
Batteries stores Electric Energy
Flywheels stores Mechanical Energy
Dams stores Gravitational Energy
Water heaters stores Thermal Energy
Cash is stored in Banks
Cash equivalents are stored in bonds, commercial paper, and other notes.

## Slide 23: Definitions: Operational Energy
Operational Energy: Energy that is consumed for transformation between forms of energy
Thermal Energy
Mechanical Energy
Radiant Energy
Electric Energy
Chemical Energy
Elastic Energy
Sound Energy
Gravitational Energy
Nuclear Energy
*
Accounting equivalent: Expenses for a period that does not accrue or accumulate.
* This transformation is the predominant source of most GHG emissions

## Slide 24: Definitions: Embodied Energy
Accounting Equivalent: An asset is a resource controlled by the entity as a result of past events and from which future economic benefits are expected to flow to the entity. (IFRS)
  Assets are accumulated by following capitalization rules.
Electric Energy
Chemical Energy
etc…
Operational Energy
Embodied energy
(at Point A)
Embodied energy
(at Point B)
Mechanical Energy
i.e., petrol in a truck
Embodied Energy: Energy that was consumed in the past but whose benefits are in the future.
  Embodied energy is accumulated operational energy.
  It can be transported between two points
  Embodied energy follows rules of embodiment, paralleling rules of capitalization.

## Slide 25: Energy also has embodied energy attributes!
25
It takes energy to produce energy
It takes energy to transport energy
Point A
Point B
Mechanical Energy
i.e., petrol in a truck
Electric Energy
i.e., ancillary services, such as demand or capacity charges
Drilling Oil
Refining Oil
Petrol
Mining Coal
Generating
Electric Energy
Electric Energy

## Slide 26: How to create an energy asset stack (part 1)
Financial assets are organized based on flexibility, often called liquidity.
  The more options available and more flexibly the resource can be used (hence more liquid), the higher it is listed in the asset stack.
FINANCIAL ASSET STACK
Cash
Cash Equivalents
Current Assets
Inventory (Benefit derived from exchange)
Non-current Assets
Plant, Property and Equipment (PPE)
(Benefits derived from use)
High Flexibility of Use
(High Liquidity)
Low Flexibility of Use
(Low Liquidity)

## Slide 27: How to create an energy asset stack (part 2)
Entropy is a measure of energy quality, or its flexibility of use.
  Low Entropy is a measure of energy quality, or high flexibility (more options)
  High Entropy is a measure of low flexibility
High Flexibility of Use
(Low entropy)
Low Flexibility of Use
(High entropy)
Electric Energy
Electric Equivalents: Chemical
  Mechanical,
  Thermal, etc.
Current Embodied Energy
i.e., Inventory
(Embodied Energy to be exchanged
between entities)
Non-current Embodied Energy
i.e., Plant, Property and Equipment (PPE)
(Embodied Energy to be used)
ENERGY ASSET STACK
Electric Energy has the lowest entropy, so it gets listed at the top.
  “Electric Equivalents” are other forms of energy, that can be converted to electricity or embodied for exchange and use.
Embodied Energy can further be split into two categories

## Slide 28: Transactions to be modelled: Building a house
[1] Mine the coal
[4] Extract iron ore
[2] Transport coal
[5] Transport ore
[3] Generate electricity
[6] Steel production
[10] Build a house
[11] Demolish house
[13] Electric
energy recovery
[12] Landfill materials
[7] Harvest trees
[8] Transport trees
[9] Timber production
[14] Materials Recovery
Assumptions: Before commercial start (Prior to any sales activity, so no P&L, only Balance sheet)
  Scenario: Build a house with steel and timber; demolish it before a sale.
  All energy is embodied

## Slide 29: Double Entry Notation: Mining coal
Transaction | Journal Entry | Debit | Credit
[1] Mine the coal | Fuel energy |  | ↑
 | Embodied energy (EE) of coal | ↑ | 
Energy Flow
Statement
(-) Fuel energy
Fuel energy
Opening
Energy Balance Sheet
Closing
Energy Balance Sheet
EE coal
Representation on
Energy Balance Sheet and Energy Flow Statement

## Slide 30: Numerical Example
Row | Transaction | Journal Entry | Debit (in MJ) | Credit (in MJ)
2 | [4] Extract iron ore (China) | 3 Fuel energy |  | 375.00
3 |  | 4 Embodied energy (EE) of iron ore | 375.00 | 
4 | [5] Transporting ore (China => UK) | 3 Fuel energy |  | 3,500,000.00
5 |  | 4 Embodied energy (EE) of iron ore | 3,500,000.00 | 
6 | [6.1] Steel production (Teeside, UK) | 3 Fuel energy |  | 108,000.00
7 |  | 4 Embodied energy (EE) of iron ore |  | 3,500,375.00
8 |  | 5 Embodied energy (EE) of steel | 3,608,375.00 | 
9 | [6.2] Transport steel (Teeside => Oxford) | 3 Fuel energy |  | 522.00
10 |  | 5 Embodied energy (EE) of steel | 522.00 | 
11 | [7] Harvest tree (Sweden) | 3 Fuel energy |  | 4,500.00
12 |  | 1 Tree farm (Intrinsic Energy) |  | 0.28
13 |  | 4 Embodied energy (EE) of tree | 4500.28 | 
14 | [9.1] Timber production (Sweden) | 3 Fuel energy |  | 5,000.00
15 |  | 4 Embodied energy (EE) of tree |  | 4,500.28
16 |  | 5 Embodied energy (EE) timber | 950.28 | 
17 | [9.2] Transport timber (Sweden => Oxford) | 3 Fuel energy |  | 4.30
18 |  | 5 Embodied energy (EE) timber | 4.30 | 
Transactions for making steel
Transactions for making timber

## Slide 31: Manufacturing Steel and Timber
Energy Flow | Quantity (in MJ)
Beginning Energy | 0.00
Inflow | 
Tree Farm | (+) 0.28
Fuel Energy | (+) 3,618,401.30
Outflow | 
Ending Energy | 3,618,401.58
Energy Assets | Opening Balance Sheet (in MJ)
Intrinsic Energy | 
Electric energy | -
Fuel energy | -
Tree farm | -
Current Energy Assets | 
Embodied energy (EE) of steel | 3,608,897.00
Embodied energy (EE) timber | 9,504.58
Non-Current Energy Assets | 
Embodied energy (EE) of a house | -

## Slide 32: Building a house
Energy Assets | Opening Balance Sheet (in MJ) | Closing Balance Sheet (in MJ)
Intrinsic Energy |  | 
Electric energy | - | -
Fuel energy | - | -
Tree farm | - | -
Current Energy Assets |  | 
Embodied energy (EE) of steel | 3,608,897.00 | -
Embodied energy (EE) timber | 9,504.58 | -
Non-Current Energy Assets |  | 
Embodied energy (EE) of a house | - | 3,620,579.18
Energy Flow | Quantity (in MJ)
Beginning Energy | 0.00
Inflow | 
Fuel Energy | (+) 477.60
Coal Mine | (+) 1,700.00
Outflow | 
Ending Energy | 2177.60

## Slide 33: Scenario Analysis of end-of-life
[10] Build a house
[11] Demolish house
[13] Electric
energy recovery
[14] Materials Recovery
[Production]
[12] Landfill
The EBS model captures the non-linearity of the circular economy

## Slide 34: Investment options: End-of-life Options
Energy used to recycle material as compared to manufacture from virgin sources
Energy Assets | Opening Balance (in MJ) | Closing Balance (in MJ)
Intrinsic Energy | - | -
Current Energy Assets | - | -
Non-Current Energy Assets (House) | 3,620,579.18 | -
Option A: Landfill the House
Complete write-off full amount of embodied energy
Option B: Energy Recovery
Waste-to-energy of the timber for 0.28 MJ and write-off the rest.
Option C: Materials Recovery
Retain EEE of Steel and EEE of Timber
Energy Assets | Opening Balance (in MJ) | Closing Balance (in MJ)
Intrinsic Energy | - | 0.28
Current Energy Assets | - | -
Non-Current Energy Assets (House) | 3,620,579.18 | -
Energy Assets | Opening Balance (in MJ) | Closing Balance (in MJ)
Intrinsic Energy | - | -
Current Energy Assets (Steel) | - | 2,165,338.20
Current Energy Assets (Timber) | - | 4752.29
Non-Current Energy Assets (House) | 3,620,579.18 | -
Aluminum | 5%
Steel | 40%
Glass | 80%
Paper | 50%
Plastic | 40%

## Slide 35: Definitions of Carbon Categories
Intrinsic Carbon (IC): The amount of carbon stored within an energy resource that may be released during future energy work.
Operational Carbon (OC): The amount of carbon released into the atmosphere during transformations between different forms of energy.
Embodied Carbon (EC): An allocation of atmospheric carbon to an item that represents the operational carbon released in the past, plus the intrinsic carbon of the material.
Carbon Balance Sheet (CBS): A statement of carbon position that represents a snapshot-in-time of carbon owned by the entity.
Carbon Gains and Uses (CGU): A statement of carbon performance that represents the trade of carbon between entities through sales and purchase transactions.
Carbon Flow Statement (CFS): Represents real-time change of carbon. Most categories of Scope 1, 2, and 3 can be found on the CFS.
New Carbon Categories
Carbon Statements
Borrowed from the energy categories

## Slide 36: The carbon asset stack
High Flexibility of Use
(Low entropy)
Low Flexibility of Use
(High entropy)
Intrinsic Carbon
Embodied Carbon for Exchange (EC for Exchange)
i.e., Inventory
Embodied Carbon of Use (EC for Use)
i.e., Plant, Property and Equipment (PPE)
(Embodied Energy to be used)
Carbon ASSET STACK
The carbon asset stack is a translation of the energy asset stack via combustion emission factors.

## Slide 37: We start accounting for Emission Factors
 | Emission Factor (kg / TJ)
Gas Oil | 0.020
Crude | 0.021
Coal | 0.026
Source: U.K. BEIS, 2020
These factors carry an uncertainty with them!
Now we introduce the accounting of methodological choice when determining carbon emissions.
We can use Emission Factors as the ‘exchange rate’ between energy and emissions

## Slide 38: Carbon transactions (by applying emission factors to energy transactions)
Transaction | Journal Entry | Debit (kgCO2) | Credit (kgCO2)
[1] Extract iron ore (China) | IC of fuel energy (Gas Oil) | - | 7.50
 | EC of iron ore | 7.50 | -
[2] Transporting ore (China -> UK) | IC of fuel energy (Crude) | - | 73,500.00
 | EC of iron ore | 73,500.00 | -
[3.1] Steel production (Teeside, UK) | IC of fuel energy (Coal) | - | 2,808.00
 | EC of iron ore | - | 7.50
 | EC of steel | 2,815.50 | -
[3.2] Transport steel (Teeside -> Oxford) | IC of fuel energy (Gas Oil) | - | 10.44
 | EC of steel | 10.44 | -
[4] Harvest tree (Sweden) | IC of fuel energy (Gas Oil) | - | 90.00
 | IC of wood from a Tree farm | - | 1,321.20
 | EC of tree | 1,411.20 | -
[5] Timber production (Sweden) | IC of fuel energy (Gas Oil) | - | 100.00
 | EC of tree | - | 1,411.20
 | EC of timber | 1,511.20 | -
[6] Transport timber (Sweden -> Oxford) | IC of fuel energy (Gas Oil) | - | 0.09
 | EC of timber | 0.09 | -
[7] Mine the coal | IC of fuel energy (Gas Oil) | - | 9.54
 | IE of coal from a mine | - | 44.20
 | EC of coal | 53.74 | -
[8] Transport coal | IC of fuel energy (Gas Oil) | - | 0.01
 | EC of coal | 0.01 | -
[9] Generate electricity | EC of coal | - | 53.75
 | EC of electric energy | 53.75 | -
[10] Build a house | EC of electric energy | - | 53.75
 | EC of steel | - | 2,825.94
 | EC of timber | - | 1,511.29
 | EC of building | 4,390.98 | -
Manufacture of steel
Manufacture of timber
Generation of
electric energy
Assembling a house

## Slide 39: Sample Carbon Asset Stack
Carbon Assets | Opening Balance Sheet (in kgCO2) | Closing Balance Sheet (in kgCO2)
Intrinsic Carbon |  | 
Electric energy | - | -
Fuel energy | - | -
Tree farm | - | -
Current Carbon Assets |  | 
Embodied carbon (EC) of steel | 76,326 | -
Embodied carbon (EC) timber | 1,511 | -
Non-Current Energy Assets |  | 
Embodied carbon (EC) of a house | - | 77,891

## Slide 40: Sample Carbon Flow Statement
Carbon Flow Statement | Quantity (in kgCO2) | Quantity (in kgCO2)
BEGINNING CARBON | - | -
Inflow of fuel (Scope 1) |  | 
Crude | 73,500 | -
Gas Oil | 208 | -
Coal | 2,808 | -
Inflow of electric energy (Scope 2) | - | 54
Inflow of embodied carbon (Upstream Scope 3) | - | -
Timber (Category 1 Products) | 1,321 | -
Outflow | - | -
ENDING CARBON | 77,837 | 54

## Slide 41: Application: Depicting fuel choice
Carbon Flow Statement | Quantity (in kgCO2) | Quantity (in kgCO2)
BEGINNING CARBON | - | -
Inflow of fuel (Scope 1) |  | 
Crude | 73,500 | -
Gas Oil | 208 | -
Coal | 2,808 | -
Inflow of electric energy (Scope 2) | - | 54
Inflow of embodied carbon (Upstream Scope 3) | - | -
Timber (Category 1 Products) | 1,321 | -
Outflow | - | -
ENDING CARBON | 77,837 | 54
 | Carbon Content (kgCO2)
IC of fuel (Coal) | 2,808
IC of fuel (Gas Oil) | 2,160
A reduction of | 648

## Slide 42: In Summary
The GHG Protocol does not follow the rules for decision usefulness as required by the financial sector.
We developed three conditions for comparability that are necessary to be met for a metric to be decision useful to the financial sector.
We constructed an energy balance sheet by introducing double-entry bookkeeping into energy accounting.
We constructed a carbon balance sheet by applying the emissions factor to the energy balance sheet
The sheets can improve strategic decision making by enabling comparative assertions in scenario plans and forecasting.

## Slide 43: References
Glenk, G. (2023). Toward Decision-Useful Carbon Information (121). https://ssrn.com/abstract=4444037
Goldthwaithe, R. A. (1985). Goldthwaite Local banking in Renaissance Florence.pdf. 5–55. https://www.econbiz.de/Record/local-banking-in-renaissance-florence-goldthwaite-richard/10001017340
IASB. (2018). Conceptual framework for financial reporting. International Accounting Standards Board. https://doi.org/10.1007/978-1-137-00662-2_5
Jia, J. Y., Axelsson, K., Chaudhury, A., & Taylor, E. (2023). A Rapid Review of GHG Accounting Standards. In SSRN Electronic Journal. https://doi.org/10.2139/SSRN.4523132
Jia, J. Y., & Taylor, E. (2022). Designing for Comparability: A foundational principle of analysis missing in GHG emission reporting systems. https://doi.org/https://dx.doi.org/10.2139/ssrn.4258460
Jia, J. Y., & Taylor, E. (2023). The Energy Balance Sheet: Maintaining Entity-Level Comparability in Carbon Accounting.
Power, M. (2021). Modelling the Micro-Foundations of the Audit Society: Organizations and the Logic of the Audit Trail. Academy of Management Review, 46(1), 6–32. https://doi.org/10.5465/amr.2017.0212
Quattrone, P. (2005). Is time spent, passed or counted? The missing link between time and accounting history. Accounting Historians Journal, 32(1), 185–208. https://doi.org/10.2308/0148-4184.32.1.185
Sangster, A. (2016). The genesis of double entry bookkeeping. The Accounting Review, 91(1). https://doi.org/10.2308/accr-51115
WRI/WBCSD. (2004). The Greenhouse Gas Protocol: A Corporate Accounting and Reporting Standard, Revised Edition. In Greenhouse Gas Protocol.

## Slide 44: Thank You!
Jimmy Jia
Oxford Sustainable Finance Group
Oxford Net Zero
jimmy.jia@ouce.ox.ac.uk